## Slide 1
Home IV infusion pump instructions
Calgary Zone Adult HPTP
Version: 2021-11-23

## Slide 2: What you need to know about your IV and Infusion Pump

## Slide 3: Welcome

## Slide 4: Your 24 hour medication bag will look similar to this
24 hours of medication
Pump will automatically give each dose as prescribed
Pump will be programmed by your nurse

## Slide 5: You know the pump is working when…
Green light is flashing
Status bar is green and indicates “Running”
Volume will decrease as pump gives medication

## Slide 6: Power Saving Mode
The screen is blank when in power saving mode.
Press one of the white keys to display screen
Green light will continue to flash to show pump is working

## Slide 7: Keep pump running at all times
Until bag needs to be changed
Until you are seen in HPTP for reassessment
Unless you have a problem with the pump or your IV

## Slide 8: Shower or Bath

## Slide 9: Sleeping with your IV

## Slide 10: Monitor your IV site often
Red
Painful
Leaking
Swelling
If pump is not working properly

## Slide 11: Who to call:
Before 9:00pm see “Contacts” section of your booklet for how to call nurse oncall

## Slide 12: Who to call after 9:00 pm:
If unable to solve IV or pump problem: - Turn pump off - Keep tubing connected to IV and pump

## Slide 13: How to re-start your pump
Follow directions in your booklet
Turn your pump on
Wait for self-test and 6 beeps
Follow directions displayed on screen

## Slide 14: Troubleshooting
Screen Display | What to Do
Low Batteries or Batteries Depleted Pump detects drop in battery power. | Press Stop/Start Stop Pump? choose Yes. Open the battery compartment at the top of pump and replace the 4 double AA batteries. Press the power switch to turn the pump back on. Press Stop/Start Start Pump? choose Yes.

## Slide 15: Downstream Occlusion
There is a blockage between pump and IV site
Follow instructions in troubleshooting section of booklet

## Slide 16: Forgot to start your pump?
If pump has been stopped
  Press “silence” key
  Press “stop/start” key
Follow instructions in troubleshooting section of booklet

## Slide 17: Low Batteries
Change batteries if pump alarms “low batteries”
Follow instructions in troubleshooting section of booklet
Note orange colour around grey battery icon for low battery

## Slide 18: Cassette Detached
Silence alarm
Follow Help screens
Call nurse if problem persists
See troubleshooting section in booklet

## Slide 19: Pump Fault
System Fault Alarm
Open and close battery compartment
Turn pump back on
Call your nurse if alarm persists

## Slide 20: Changing your IV bag

## Slide 21: Lastly...
Ensure you are comfortable with your pump
Make a follow-up appointment
See the pharmacist before you leave
The nurse will answer any questions you have